IR RECEIVER

This circuit can operate a load such as LED, Buzzer or Relay for a period of  3 minutes through a Remote hand set. It uses the IR sensor module TSOP 1738 which operates in 38 KHz Infrared pulses.

The circuit is a Short duration Monostable  using 555 timer IC. Its trigger pin 2 is connected to the output of the IR sensor through R2 and LED. Normally the output of  IR sensor is low. But the timer IC will not be triggered because its trigger pin remains high through R3. When the remote hand set is focused on to the IR sensor and any one of the buttons is pressed, out put of IR sensor goes low and triggers the 555 IC. With the given values of the timing elements R4 and C2, output of the timer remains high for 3 minutes. By changing the value of R4 or C2 this time can be changed

Visit dmohankumar.wordpress.com for Articles and Circuits.     Website www.electroschematics.com

Visit electroskan.wordpress.com for Hobby Circuits