Low cost Pilot Lamp

This is the simple way to connect an LED in the Mains to use it as a pilot lamp. It takes little current compared to a neon lamp. It can power low efficiency as well as high efficiency LEDs including White and Blue LEDs.

The circuit is straight forward. A rectifying diode IN4007 (1A) is connected in series with the phase line. The rectified voltage is reduced to low volt by the resistor R1. Capacitor C1 filters some ripples and act as a buffer to provide continuous supply to the LED as the AC waveform swings. Resistor R2 determines the brightness of LED. With 1.5 K resistor, adequate brightness can be obtained

Important Note - The circuit is directly connected to mains and hence at lethal potential. Do not touch or troubleshoot when it is connected to mains.